White Plasma
Introduction

White Plasma is loosely based – very loosely – on the old Spectrum system “White Lightning” which is a FORTH based system designed to run on the Spectrum. White Plasma is a Colour FORTH styled system designed to run on the Spectrum Next and Spectrum 128, specifically, but will also work on a standard Spectrum.

Design Issues

The main design issue is to do with the banked RAM memory. All machines are Z80 8 bit microprocessor based, with a 16 bit address space. A Spectrum looks like this.

C000-FFFF	Fast RAM
8000-BFFF	Fast RAM
4000-7FFF	Screen Memory, slow RAM
0000-3FFF	Basic ROM

A Spectrum 128 looks like this, paging memory onto C000-FFFF.

C000-FFFF	Fast RAM	RAM / Page	RAM / Page	RAM / Page
8000-BFFF	Fast RAM
4000-7FFF	Screen Memory, slow RAM
0000-3FFF	Basic ROM

A Spectrum Next offers far more flexibility, but can operate on the same model as a Spectrum 128, e.g. paging RAM pages in and out of C000-FFFF, though its pages are 8k not 16k. I will therefore use this model for implementing White Plasma as it is compatible with both designs, albeit with a different paging system.

C000-FFFF	Fast RAM / Forth Words	Page / Forth Words	Page / Forth Words	Page / Forth Words
8000-BFFF	Fast RAM / Forth Words / Core Z80 Words
4000-7FFF	Slow Memory / Screen Memory / Dictionary / Variables / Stacks
0000-3FFF	Basic ROM

Dictionary

This FORTH has a separate dictionary and code. This is stored in the Slow RAM area (it has to share access with the video display) and grows down. It is a list of names and addresses of words stored in High Memory.

It is possible to move the start point of the dictionary up in memory to create a larger dictionary, as the dictionary starts immediately below the core words.

So in the standard setup, the dictionary’s first byte, working downwards is $7FFF.

Core Words

Core words are words represented by the values 00-7F. These words are implemented either as virtual codes, or in Z80 Assembler. They occupy one byte in code space.

Their implementation starts at the core word address. This is currently at $8000 but can be any address in 4 page steps (e.g. $8400,$8800).

Direct Words

Direct words are when either (1) the word to be called is in 8000-BFFF or (2) the word to be called is in $C000-$FFFF and the page for that word is the same as the page for the word it is being called from.

These words consists of lists of calls to either Core Words (1 byte, 00-7F) or Direct Words (80-FF xx). In the latter, the two bytes represent the start address of the routine.

Note: in the page switch words (e.g. words in $C000-$FFFF) the start address must have the lower 3 bits clear, because page addresses are encoded into one word.

Page Switch Words

Sometimes the compiler has to switch pages to execute a word. There are two occasions where this happens.

If the compiler does not know which page the word to be executed is in, for example if it is executing a word indirectly. The best solution for this is to push it to the return stack (see the return section).

The second occasion is where it does know which page it is in, but the selected page (in $C000-$FFFF) is not currently selected. In this circumstance, it uses the [farcall] keyword to call the method, which includes the relevant page switching.

This has a single 16 bit parameter. Bits 0-4 indicate the page number, which is not the same as the Spectrum Next/128 page number. Bits 15-10 are the address to be called.

This address is masked out and shifted right twice, and ored with $C000. This gives an address of 11xx xxxx xxxx x000.

Not all addresses can be called directly, therefore when creating code in $C000-$FFFF it should be padded out to 8 byte gaps with [nop]

Also, when compiling code, the programmer needs to use the far access functions . These functions should not generally be used to access memory in applications.
Return from Calls

When a direct word is called, its return address is pushed on the stack ($8000-$FFFF). The [farcall] function pushes the same value on the stack but with bit 15 clear ($0000-$7FFF). This indicates that there is a further value to be popped off the stack, which is the page number to set it back to – bit 15 is set when the actual return is done.

As a consequence of this is it is necessary to be very careful with r> and r>. For example variable is defined as r>. This will only work if variable is called using a direct call. It should be, if it is in a module.

Issues

I have dealt with code across the pages, but not with data. The issue with data is that any address in the memory space is 21 bit , 16 + 5.

The solution are the module and endmodule macros. This defines (or end) a module, which is a group of methods that access data. Using these words an error is generated if the page at module time and the page at endmodule time is different (or if it crosses the BFFF-C000 boundary) If it is the same, then data can be freely accessed in that module using @ c@ ! c! and so which operate as normal.

Any data access which happens outside the module has to be done through specific words created to do so, which are part of the module. The programmer must enforce this.

Words can be defined using the modifier macro private which sets the private flag in the dictionary. This means the dictionary can compress on endmodule being executed, removing all words that are not useable from outside it.

So in this simple bit of code.

module
demo private 42 emit ;
start demo ;
endmodule

start will be in the dictionary and demo will not. This also conveniently reduces the size of the dictionary.

System Information Block

This is placed at the bottom of the load space, this address can be accessed via [[sysinfo]], and is normally placed at $6000. [[sysinfo]] is not a keyword, it is produced by the compiler and generated as a literal as normal.

Offset	Usage
+0,+1	Temporary value used in keyword synthesis.
+2,+3	The core address ($8000), the dictionary starts at core-1
+4,+5	Next free dictionary byte, working down.
+6,+7	Next free FORTH code byte, working up.
+8	Current page number of code. 0 = Default page, increments up.
+9	Start address page (of _main)
+10,+11	Start address (_main address)
+12	Screen width in characters (16)
+13	Screen height in characters (12)

Dictionary

Remember the dictionary goes down in memory.

Offset	Usage
0	Offset to the next word in the dictionary (subtracted), zero if at the end of the word, call this value ‘n’
-1, -2	The address or short code, so either -1 contains $00-7F and -2 contains $00, or -1 contains $80-$FF and -2 contains the low byte.
-3	Bit 7: set if macro. Bit 6: set if core word, Bit 5: set if private word ; Bits 0..4: page number of the word.
-4	First character of name, 6 bit ASCII, bit 7 set if not the last
-5	Second character of name, 6 bit ASCII, bit 7 set if not the last
-n+1	Last character of name, 6 bit ASCII, bit 7 cleared.

Compiler

Obviously the system compiler works perfectly normally, using the colour word system

- Yellow – always execute
- Green – compile, unless macro in which case execute
- Red – define word here
- White – comment
Equally obviously for the text compiler we cannot do that, because we don’t have the colour editor or the run time environment.

{ }	ColorForth does not have curly brackets, so these delimit comments
in the same line (e.g. you cannot have { and } on different lines.
:<word>	Defines a new word at this point in memory. If the word is present
compiling is halted until the next definition.
macro	Makes the last defined word a macro
private	Makes the last defined word private
variable	Compiles [variable] and an 2 byte space. Marks last word private.
<decimal>	Compiles the value as a literal or a call if in the dictionary
$<hex>	Same as decimal, except in base 16, obviously.
If …. then	Structure in ColorForth. Cant nest. ; closes then. TOS test destructive.
For … next	Structure in ColorForth, takes one parameter the count.

Compiler Information

This information is provided in a seperate class

- The Load address ($6000)
- The Core address ($8000)
- The Size of the Z80 Core Binary File (0, in the VM)
- Which ‘short words’ are available.
Word Groups

Group 0 is the core word set and is mandatory. Group 1 is not required, but is highly advised to be implemented in code for speed reasons.

Note that the booting code contains [[sysinfo]] which is a compiler word (pushes Load address on Data stack), it is neither a keyword or a direct word.
Core Word Set

word	Description
[break]	Stops the processor. By convention this is $00 so if addresses go haywire and emulator memory is initialised to $00 it will stop rapidly.
;	Return , as described with 2 levels.
!	16 bit store
[brzero] xxxx	Branch to address xxxx if the top value is zero, destructive.
[farcall] xxxx	Far call as described in text
[literal] xxxx	Push literal xxxx on the stack
[nop]	Do nothing, used for padding.
[stackreset]	Reset stacks to default values (done at reset)
@	16 bit read
+	Add 2 values
>r	Data stack → Return Stack
2/	Arithmetic shift right 16 bit
cursor!	Set cursor position.
keyboard@	Read keyboard, 8 = backspace, 13 = CR, 16-19 = up/down/left/right 20-23 is colours 0-3 32-95 is returned for ASCII values.
nand	Logical Nand of 2 values
page@	Read currently selected memory page number
page!	Set memory page number. Maps 0,1,2 to available pages.
r>	Return Stack → Data Stack
screen!	Write to screen position. Bits 6 and 7 are colour, 5-0 are characters.

Group 1 Words

not	dup	drop	swap	over	nip
c@	c!	0=	0-	1-	1+	2-
2+	-	+!	+*	2*
and	or	xor	0<	<<

Constants	0,1,-1,2
Loop Help	[next]

Note : << and 2* are synonyms, but >> and 2/ are not. << >> are logical not arithmetic shifts

Group 2 Words

4*	8*	16*	256*	16/	256/	>>
i	0>=	0>	0<=	abs	min	max

Constants	4,8,10,16,100,256
Variable Help	[variable]

Group 3 Words

*	u/	umod	rot	>	<	>=
<=	=	<>

Group 4 Words

far@	far!	C,	,	1,	[sysinfo]

Macros	do,until,if,then.for,next

Console I/O words

colour	color	cr	emit	green	red
white	yellow	cls	home	u.